## Slide 1: Arduino-Based Distance Measurement System
Using a Servo Motor and Ultrasonic Sensor

## Slide 2: Introduction
This project aims to measure distance using an ultrasonic sensor and a servo motor to scan the environment.
Components:
- Arduino
- Ultrasonic Sensor (HC-SR04)
- Servo Motor

## Slide 3: Components Required
- Arduino board
- Ultrasonic sensor (HC-SR04)
- Servo motor
- Jumper wires and breadboard

## Slide 4: Circuit Diagram
Wiring Connections:
- Trig Pin to digital pin 11
- Echo Pin to digital pin 12
- Servo motor signal to digital pin 13

## Slide 5: Code Explanation (Part 1)
Code Section: Importing Libraries and Setting Up Pins
#include <Servo.h> - Servo library
const int trigPin = 11;
const int echoPin = 12;
Explanation: This section imports the Servo library and defines pins for the ultrasonic sensor.

## Slide 6: Code Explanation (Part 2)
Code Section: Setting Up Functions
void setup():
- Sets up pin modes and attaches the servo.
- Serial communication initialization allows data output to the Serial Monitor.

## Slide 7: Code Explanation (Part 3)
Code Section: Loop Function and Servo Motor Movement
- Uses for loops to rotate the servo motor from 15° to 165° and back.
- Calls calculateDistance() function to read ultrasonic sensor values for each angle.

## Slide 8: Distance Calculation Function
Focus on the calculateDistance() function:
- Uses pulseIn() to measure the echoPin signal duration.
- Calculates distance with: distance = duration * 0.034 / 2

## Slide 9: Serial Output
Explanation of Serial Output:
- Data format sent over Serial Monitor: angle,distance
- Comma-separated values facilitate indexing for Processing IDE.

## Slide 10: Video Demonstration
Screenshots from the video:
- Demonstrates system in action.
- Shows data display and sensor rotation.

## Slide 11: Applications
Potential Applications:
- Obstacle detection
- Robotic navigation
- Environmental scanning

## Slide 12: Conclusion and Future Work
Summary:
- Successfully measured distance using servo and ultrasonic sensor.
- Possible improvements: using multiple sensors, integrating with a display.